## Slide 1: SDI Team 23: Programmable Communication Group Error Correcting Codes in Amateur Radio Satellite Telemetry Category 2 – Project with active research agenda
December 7, 2013

## Slide 2: What is amateur radio satellite telemetry?

## Slide 3: Problem Statement
Automatic repeat request is not used, so strong signals are transmitted to ensure telemetry packets are received without error.
Strong signals require high power consumption. This leads to expensive and esoteric means of communication.
Miniaturized satellites would be more accessible to prospective amateur satellite operators if the equipment involved weren’t so expensive and esoteric.

## Slide 4: Proposed Solution Concept
Use a more power-efficient bandpass digital modulation scheme
  BPSK instead of Bell 202 BFSK
Implement forward error correction (channel coding)
  Convolutional code – corrects random errors

## Slide 5: Current Progress
Developing three digital loopback systems
  Each have bit error rate tester (BERT)
  Each have AWGN channel (random noise)
  System A (more power-efficient modulation)
    Modulation scheme: 1200 b/sec BPSK
    Channel coding: none
  System B ( System B + forward error correction)
    Modulation scheme: 1200 b/sec BPSK
    Channel coding: convolutional FEC

## Slide 6: Current Progress
Chart: Amateur Satellite Telemetry BER Performance in AWGN Roundup
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
1200 b/sec BFSK | 0.2456 | 0.21 | 0.18333 | 0.15 | 0.1352 | 0.1 | 0.0804 | 0.05 | 0.035
1200 b/sec BPSK | 0.08399 | 0.06059 | 0.0397 | 0.0253 | 0.0147 | 0.006099 | 0.0019 | 0.0007999 | 0
1200 b/sec BPSK-FEC (hard-decision) | 0.3974 | 0.2942 | 0.1124 | 0.02021 | 0.0008044 | 0 | 0 | 0 | 0
1200 b/sec BPSK-FEC (soft-decision) | 0.2802 | 0.1057 | 0.01036 | 0.0002011 | 0 | 0 | 0 | 0 | 0

## Slide 7: Current Progress
Signal-to-noise ratio (dB) | 1200 b/sec BFSK THEORETICAL | 1200 b/sec BPSK | 1200 b/sec BPSK FEC (hard-decision) | 1200 b/sec BPSK FEC (soft-decision)
8 | 3.50e-2 | 0 | 0 | 0
7 |  | 7.999e-4 | 0 | 0
6 | 8.04e-2 | 1.9e-3 | 0 | 0
5 |  | 6.099e-3 | 0 | 0
4 | 1.352e-1 | 1.47e-2 | 8.044e-4 | 0
3 |  | 2.53e-2 | 2.021e-2 | 2.011e-4
2 | 1.833e-1 | 3.97e-2 | 1.124e-1 | 1.036e-2
1 |  | 6.059e-2 | 2.942e-1 | 1.057e-1
0 | 2.456e-1 | 8.399e-2 | 3.974e-1 | 2.802e-1

## Slide 8
Current Progress
Simulink Model of BPSK Modem

## Slide 9
Current Progress
Chart: Our 1200 b/sec BPSK BER Performance vs. Theoretical in AWGN
| 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26
Our BPSK | 0.49139 | 0.08321 | 0.05071 | 0.02951 | 0.0126 | 0.004601 | 0.0014 | 0.0002 | 0.0001
Theoretical BPSK | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 10
Polarity Reversal at 10 dB
AWGN at 10 dB causes 180 phase shifts resulting in the PLL tracking in the wrong direction
IMPLICATION: Necessitates need for differential encoding

## Slide 11
Phase Error Response to Frequency Step
PLL phase error becomes Amplitude Modulated after frequency step
IMPLICATION: Necessitates need for AGC

## Slide 12: Future Work – Short-term Integrate FEC and BPSK simulations

## Slide 13
Future Work
___Winter Break___
Complete System C simulation (BPSK + FEC)
Develop AWGN core
Develop BERT (software)
Develop USB-R232 HDL
Begin converting Simulink models to HDL models
___Senior Design II ___
FPGA Implementation of System B & System C
Test and verification of modem requirements.
Comprehensive budget link analysis to assess reduced power consumption

## Slide 14: SDI Team 23: Programmable Communication Group Error Correcting Codes in Amateur Radio Satellite Telemetry Category 2 – Project with active research agenda
December 7, 2013