## Slide 1: SDI Team 23: Programmable Communication Group Concatenated Codes in Amateur Radio Satellite Telemetry Category 2 – Project with active research agenda
December 7, 2013

## Slide 2: What is amateur radio satellite telemetry?

## Slide 3: Problem Statement
Automatic repeat request is not used, so strong signals are transmitted to ensure telemetry packets are received without error.
Strong signals require high power consumption. This leads to expensive and esoteric means of communication.
Miniaturized satellites would be more accessible to prospective amateur satellite operators if the equipment involved weren’t so expensive and esoteric.

## Slide 4: Proposed Solution Concept
Use a more power-efficient bandpass digital modulation scheme
  BPSK instead of Bell 202 BFSK
Implement forward error correction (channel coding)
  Concatenated codes
    Block code – corrects burst errors
    Block interleaving – improves block code
    Convolutional code – corrects random errors

## Slide 5: Current Progress
Developing three digital loopback systems
  Each have bit error rate tester (BERT)
  Each have AWGN channel (plus burst noise)
  System A (most prevalent today)
    Modulation scheme : 1200 b/sec Bell 202 BFSK
    Channel coding: none
  System B (more power-efficient modulation)
    Modulation scheme: 1200 b/sec BPSK
    Channel coding: none
  System C ( … plus forward error correction)
    Modulation scheme: 1200 b/sec BPSK
    Channel coding: concatenated FEC

## Slide 6: Current Progress